## Slide 1: Busting The Pileup
Kevan Nason
N4XL

## Slide 2: Really?!?
Notes: Experience of Audience compared to me
Looking beyond what people normally think of as how to bust a pileup
More contesting oriented than you might be used to

## Slide 3: Myths
To bust a huge pile up you need:
  An amplifier
  A 70 foot tower
  A friend with an amplifier and 70 foot tower
  Luck

## Slide 4: Truths
You can bust a pile up with:
  100 watts (some regularly do it with 5)
  A decent antenna –
  wire, beam or vertical
  Experience

## Slide 5: Thoughts…
"With experience comes knowledge and cunning. I can't stand here and tell you the secrets, as many of them are second nature to me now."
-- KR0Y/5
"The best of the best gained their winning edge practicing the basics over and over in numerous forgettable events, often using inadequate radios and second-rate antennas. Discovering how to overcome such obstacles are lessons never forgotten."
-- NCJ Profile of N6RO

## Slide 6: Standard Things to do…
Listen for where DX is listening
Use band scope
Split VFO’s
Get a good antenna(s)
Get an amplifier
Time your call for quieter periods

## Slide 7: Exploring Other Thoughts…
  Know your stations limits
  Know your rig
  Antenna options
  Logging software aids
  Additional operating skills

## Slide 8: Station Limits
You Gotta Hear ‘em
To Work ‘em
If all you can hear is silence when the uproar stops then leave and try later

## Slide 9: Station Limits - Not trying is sometimes faster
  If they are a common call or multiplier and/or only two or three people calling then
  Shut up and let other guy go first
  If you are both on the same freq or have the same signal strength, or if the DX op is not highly skilled fighting for it only results in many “Again?” requests

## Slide 10: Station Limits - DX University – Using Propagation to Your Advantage
  Calling DX when conditions to your area are poor doesn’t usually make sense
  Not calling requires discipline
  Calling when you can just hear the signal “in there” is tempting but… “dangerous” and possibly embarrassing… if you are actually called and can’t hear the reply.

## Slide 11: Station Limits - Not trying at all
If he’s in AF, only S5 or so, and only answering EU often it is not worth wasting time. You only cause QRM
  You are on the side of his beam so much weaker to him than EU is
  But hey… You never know. Try a couple of times. You might get lucky.

## Slide 12: Station Limits - Contest situation
Big pile up and you have a modest station
Look at “Mult is worth X.X Q’s” ratio
Is it Saturday? Is he likely to still be there tomorrow and hungry for Q’s?

## Slide 13: Station Limits
K1AR Contesting Tip #60
Don't ever get so intimidated by the size of a pileup that you simply tune by the station without calling. We all have a story or two about the time we broke trough a pileup without a clue how our station pulled it off. Here's the answer: operating skill! … If you don't at least try to call them, you absolutely won't work them!

## Slide 14: Know Your Rig
If you can’t hear the DX say your call through the QRM you can’t work them
Practice actually using your rig to fight QRM on pileups before you need those skills for real

## Slide 15: Know Your Rig RX adjustments for best IMD and dynamic range
No noise blanker
No preamps – especially on low bands
No RX DSP processing
Use narrow roofing and IF filters. Max out filter load in your rig
Use RF gain
Fast AGC or even turn it off

## Slide 16: Know Your Rig
Filter use – You gotta hear him to work him
  500 to 2,500 Hz response works good for SSB
  Lower CW tones work better
    Ear can hear a 30 Hz tone difference better at 500 hz than it can at 800.
    Easier to differentiate between many signals on the same band.
Experiment with RX equalization – Formant pass works for me
APF (SAF) can make signal pop out of the mess

## Slide 17: Know Your Rig TX adjustments
K3WWP - Working DX- Tips
Be sure your signal is as clean and crisp as possible and your keying is as close to perfect as possible. DX stations often mention that it is not always the strongest signal that is easiest to copy in a pileup, but often a weaker clean signal with perfect keying is easier to copy. If you have a memory keyer, use that to send your call. It is possible to get nervous when trying for some rare DX, and be sloppy sending even our own call

## Slide 18: Know Your Rig TX adjustments
SSB - Use Contest audio
  High freq’s count (500 to 2,000 Hz). That is place to focus
  Heil element and/or TX equalization
Get a DXer or Contester to critique you – not a Rag Chewer. They often don’t like contest audio and steer you wrong.
Use Speech Processor – Don’t overdrive it though

## Slide 19: Antenna Options
Two or more antennas per band
  You do understand about Take Off angles and HFTA, don’t you?
Fast antenna switching capability
Receive antennas to reduce QRM and improve S/N ratio
  K9AY Loops, Flags, etc. fit in small lots
  Try Dipoles, Verticals, Beams or BOG as a receive antenna.

## Slide 20: N1MM aids
Spots
  Pre-Filter so only get from your region
  Post-Filter so only show mults
  Never trust spotted call signs – Always verify them !

## Slide 21: N1MM aids Mult & Q window

## Slide 22: N1MM aids Mult & Q window
DX University –
  How to Gain an Advantage in a Pileup –
    The appearance of a rare DX station on the ham bands usually results in a pileup of DXers calling the DX station in an attempt to add a band-mode counter to his or her DX total
Set Available Mults & Q’s filter to only show mults
Keep an eye on them. If S&P jump using keyboard shortcuts

## Slide 23: N1MM aids Mult & Q window

## Slide 24: N1MM aids Neat Tips…
Change Freq just by typing it in
  DX was simplex on 7057 and says “Now listening 7238 and this frequency.”
  Type “7238”, CTRL-ENTER and you are now split with XMIT VFO instantly on 7238
CW Offset
  Everyone who clicks on a spot lands on the same exact freq.
  Can tell N1MM to apply a random offset to spots so you aren’t in the mass of people

## Slide 25: N1MM aids Tips…
If use a voice keyer trim all silent parts at start and stop of voice message
  best control of exactly when call inserted
  Sometimes 0.2 seconds does matter
  The ear will naturally latch on to the first thing it can clearly hear
  Want XMTR off as soon as call is done so can hear DX come back to you
  Voice message to give call sign ONLY ONCE. Push F key twice if want your call twice.

## Slide 26: N1MM aids Neat Tip…
Populate the log entry window with call and exchange. If exchange is a number and you don’t get through, CTRL-U increases number by 1.

## Slide 27: Operating Skills
BE FLEXIBLE!!
There is no “formula”
What works one time may not the next

## Slide 28: Operating Skills Phonetics
  Use standard – Many foreign stations barely know enough English for a contest type QSO
  Know alternate numbers in that countries language
  If trouble getting message through, use different phonetics
    For Europeans having trouble with Lima I’ve found London works well
    For Japanese Tokyo often works if Tango doesn’t
    For Spanish speaking Santiago works when Sierra doesn’t

## Slide 29: Operating Skills K1AR Contesting Tip #23
  Try varying the phonetics you use in pileup calling. Sometimes a different word will help differentiate your call from the others. Sharp, piercing words are usually more effective. For example, GERMANY is probably better than GULF, or consider DENMARK instead of DELTA …

## Slide 30: Operating Skills K1AR Contesting Tip #15
  SOUND EXCITED!!
  There are many factors to consider when trying to break a big pileup in a contest. One aspect sometimes forgotten is the way you call a station. If you sound like you really want to work someone (without getting carried away), you're more likely to beat the majority of stations that call with a more "layed-back" approach

## Slide 31: Operating Skills DX University Tip – N7NG
  How To Gain An Advantage In A Pile-up
  Another way of gaining an edge is to take advantage of others’ errors... Every operator who feels he absolutely must comment about something on the DX station’s frequency (“he’s listening UP. UP, UP” etc.) can be another plus for you. The more guys who are transmitting on the DX frequency, the more who AREN’T transmitting in the pileup... Moreover, when the DX is covered with QRM, the fewer people will actually call. I have always made it a point to call – in the pileup – during these times, even if I temporarily can’t hear the DX station.

## Slide 32: Operating Skills DX University Tip – Faulty Timing, N7NG
  Only Send Your Call Once
  Normally, the DX station says something like “TU UP,” and a caller responds by sending his callsign, and [perhaps] the DX station responds to him. On occasion though, the caller might decide to send his callsign more than once. Often when he does this, the DX op apparently expecting only one call, starts responding while the caller is still transmitting. Since the caller hadn’t completed his call, there is considerable time- wasting confusion.

## Slide 33: Operating Skills DX University Tip – N7NG
  Encore Performance:
  What Are You Listening For?
  …DX station is on CW, and he is saying “up.” What does that mean? With a small pileup on CW, “up” generally means up about 1 kHz. With a large pileup, though, saying “up” might mean many things. With a large pile, the DX op will need to spread his listening range in order to hear anyone in the mess, so he can’t be just listening “Up 1”

## Slide 34: Operating Skills DX University Tip – N7NG
  … for the week or so just before the big DX contests, many of the stations setting up for the contest will check out their equipment by working as many folks as possible. At these times they may also operate on the WARC bands (30, 17, 12) which are not available for operation in the contest itself. They often stay at their locations for a few days after contests also…

## Slide 35: Operating Skills K1AR Contesting Tip #19 - Attitude
  … something that can help your contest score nearly as much as a big signal… focus and utter concentration. Whether you're trying to lift a heavy weight in a gym or push a few more QSOs out of your station, the key is diligence and unabated attention to the task at hand... If you apply the same techniques to contesting that you do in your other endeavor, your scores will climb--and without a single db of added signal strength

## Slide 36: Operating Skills
  CW
    The ear tends to follow a changing pitch.
    Tune frequency slightly while transmitting your call.
    Good CW ops tend to use wider rig filters and use the filter between their ears. This idea doesn’t work well if the DX op has a narrow filter.

## Slide 37: Operating Skills DX University Tip – N7NG
  Will DX tune up or down while working a pileup?
  …right-handed operators (most of us) … tune with their left hand… it’s far easier for me to tune the main knob counter- clockwise (to the “left”) than clockwise, i.e., up in frequency…

## Slide 38: Operating Skills DX University Tip – N7NG
  For guys who have never been on the other end, it’s difficult to explain what it sounds like when you have 20 or more guys all calling on the same frequency at the same time. It is literally impossible to pick out a call or sometimes even a letter. Some DX operators will just sit there, waiting for repeated calls until they finally get one—and end up with one QSO every 2-3 minutes. The good ones will do something [else]. .

## Slide 39: Operating Skills Understanding the Running Op
  What tools prove effective in breaking a pileup are often dictated by the experience of the running op
    Inexperienced ops are overwhelmed by the wall of noise and often reward tail enders or waiting for the rush to get over. Rate is low
    Experienced will pick out a partial call and use that to keep rate up

## Slide 40: Operating Skills How Badly Do You Want The Q?
  DX University Best Practices for Courteous and Efficient DXing –
  Rule #7
  Respond only if the DX operator calls you. One letter or number of your call is NOT enough reason to call

## Slide 41: Operating Skills How Badly Do You Want The Q?
You are listening and haven’t called yet and you hear “Who’s the Four?” -- Jump in there
“Who’s the 5 Xray?” N4XL. I automatically do this if he didn’t get an answer to his first try and repeats his request for the 5X.
“Who’s the 7 Whiskey?” If he says it a second time I wait two seconds and say N4XL
DX University – How We Will Operate - We will persist with a callsign, then QRZ or NIL. No exceptions. We will NOT call another station until we solicit another Q. Any deviation from this routine is a green light for DXers to call out of turn. -- Don’t believe this

## Slide 42: Operating Skills How Badly Do You Want The Q?
  Doing those things may get you black listed by the op and you’ll have to leave and come back later—but, usually, if you do it with respect (i.e.: understanding the DX wants to keep rate up and you are really helping him get on that track) you will get an answer.
DX University – How To Work Us - Reiterating, we will not work stations who are:
  Calling out of turn when we are trying to work someone else
  Calling out of the called area - study the pileup and wait for your turn
  Calling with an obviously wrong partial callsign - use the time to study the pileup

## Slide 43: Operating Skills How Badly Do You Want The Q?
DX University – Helpful Hints # 59 - In the end, these apparent disruptions aren’t nearly as bad as they seem to DXers. If the QSO rate is good, and the accuracy is high, the problem is primarily aesthetic, but it doesn’t sound good to the sensitive ears of deserving DXers. This week’s hint for DXers is to think about what is happening in these major pileups, try to understand why people do what they do. And, try very hard to disregard those factors that don’t really affect your probability of getting in the DXpedition log. It is really to your advantage to devise a way around these situations while others are busy hand-wringing -- N7NG

## Slide 44: Operating Skills How Badly Do You Want The Q?
  Spot Her
  She might not be aware the band has opened to NA. Logging programs often tell you when you’ve been spotted. If she has been working EU for a while and sees a W4 spotted him she may switch and call NA. I sometimes spot, move on to work a couple more q’s, and then check back to see what happened after my spot.

## Slide 45: Operating Skills Examples
  Video of two ops running pileups. One very good, the other competent.
EJ7NET on Gola Island
https://www.youtube.com/watch?v=P6Hn3jqCXSI
8R1PY -2012
https://www.youtube.com/watch?v=655ZhrA26as

## Slide 46: Operating Skills Tips…
Advice from
  HC8N
  K5TR
  See external Microsoft Word file “Contesting Wisdom” for the advice

## Slide 47: Summary
Know your rig. Use it so you can hear the DX
Be focused and aggressive
Evaluate the skill level of the DX op and choose your tools with that in mind
Lastly, don’t give up! Come back later when propagation has changed and try again

## Slide 48: Thanks – and Good Hunting!